## Slide 1: HARDWARE IMPLEMENTATION OF REAL TIME COMMUNICATION USING UART WITH AES 128 ENCRYPTION/DECRYPTION IN VERILOG

## Slide 2: Advanced Encryption Standard (AES)
Block cipher: processes blocks of texts of fixed size of 128 bits (16 bytes) and outputs a new block of the same size.
Works on the methods of substitution and permutations.
Symmetric encryption algorithm, same key for both encryption and decryption which is confidential to sender and receiver.

## Slide 3
Figure: AES Encryption and Decryption

## Slide 4: AES Add Round Key
The input data is bitwise Xor’ed with key in this stage

## Slide 6
Simulation: ADD Round Key

## Slide 7: Substitution Bytes ( ) Transformation
Each byte substituted using a well-defined substitution box called S-box.
Contains mapping of each byte from 00 to FF.
For example: {56} is substituted by looking at row 5 and column 6 in the 16 * 16 S-box, the substituted byte is the intersection of row and column.
Data is Mapped to 4*4 matrix

## Slide 8
Fig : AES Substitution box

## Slide 9: Inverse Substitution Bytes ( ) Transformation
Inverse of the substitution Bytes Transformation.
Inverse Substitution Box is the inverse mapping of the substitution box.
For example: The byte {B1} is transformed to {56} after this operation.
{56} {B1} (Encryption)
{B1} {56} (Decryption)
Data is Mapped to 4*4 matrix

## Slide 10
Fig : AES Inverse Substitution box

## Slide 11: Verification of sub byte and inverse sub byte transformation

## Slide 12: Shift Rows ( ) Transformation
The 16-byte data ( or say 128-bit data) is arranged in a 4 x 4 grid.
In each of the four rows,
  1st row remains unchanged.
  2nd row, each byte is shifted one position to the left.
  3rd row, each byte is shifted two positions to the left.
  4th row, each byte is shifted three position to the left.

## Slide 13
A1 | A5 | A9 | A13
A2 | A6 | A10 | A14
A3 | A7 | A11 | A15
A4 | A8 | A12 | A16
A1 | A5 | A9 | A13
A6 | A10 | A14 | A2
A11 | A15 | A3 | A7
A16 | A4 | A8 | A12
Fig : 4 x 4 array of input data
Fig: 4 x 4 array of shifted data

## Slide 14: Inverse Shift Rows ( ) Transformation
Similar to the Shift Rows ( ) transformation in functionality, except the rows are shifted in the reverse order.
​In each of the four rows,
  1st row remains unchanged.
  2nd row, each byte is shifted one position to the right.
  3rd row, each byte is shifted two positions to the right.
  4th row, each byte is shifted three position to the right.

## Slide 15
Verification of shift row() and inverse shift row() transformation

## Slide 16: Mix_Column
Performs mixing of column wise data in finite field (GF^8)

## Slide 17: Operation

## Slide 18
Irreducible Polynomial

## Slide 19
6
0
8 bit
5
4
3
2
1
0
XOR
1
0
0
0
0
1
1
0
1
1
8 bit in
8 bit out
7
Multiplication by 2

## Slide 20
Multiply_02
8 bit in
XOR
8 bit out
Multiplication by 3

## Slide 21: Inverse_Mix_Column
Performs mixing of column wise data in finite field (GF^8)

## Slide 22
8 bit in
XOR
8 bit out
Multiply_02
Multiply_02
Multiply_02
XOR
Multiplication by 0B

## Slide 23
Multiply_0D
Multiply_0E
Multiply_09

## Slide 24
Simulation: Mix Column and Inverse Mix Column
ASCII
Hexadecimal

## Slide 25: Key EXPANSION
(2)

## Slide 26
Components
KEY EXPANSION
Three rightmost bytes are always 0.
Multiplication defined over the field GF().
Multiplication defined over the field GF(2^8).
Varies for each iteration of key expansion round.
RCON Matrix:
Components
KEY EXPANSION
+ + + 1

## Slide 27
Components
KEY EXPANSION
Performs byte substitution on input word with word from AES Substitution Box.
RotWord performs a one-byte circular left shift on a word.
RotWord:
Substitution Byte:
This means that an input word [B0, B1, B2, B3] is transformed into [B1, B2, B3, B0].

## Slide 28: Simulation

## Slide 29: UART
UART stands for Universal Asynchronous Receiver/Transmitter
Data transmitted in Serial stream reducing number of wires used to transfer data
Transmitter/Receiver agree on certain parameters:
    Baud Rate (9600 bits/sec)
    Number of data bits (8 bits)
    Parity bit (0)
    Stop bits (1)
    Flow Control (None)

## Slide 30
UART PROTOCOL

## Slide 31
UART Transmitter
State Machine

## Slide 32
UART Receiver
State Machine

## Slide 33
Figure: AES Encryption and Decryption

## Slide 34
Encryption
9
Rounds?
No
Yes
128 Bit Input
128 Bit Output
Add Round Key
Substitution Bytes
Add Round Key
Mix Col
Shift Row
Substitution Bytes
Shift Row
Add Round Key

## Slide 35
Initial
Mid
Final
Circuits
Add Round Key
Substitution Bytes
Add Round Key
Mix Col
Shift Row
Substitution Bytes
Shift Row
Add Round Key

## Slide 36
Initial
Mid
Final
Mid
Mid
Mid
Mid
First
Between
Last
FSM Circuits

## Slide 37
Encrypter
First
Between
Last
Between
Between
128 Bit Processed Data
Completion Status
Data
Data
Data
Data
Data
Data_in
Data_out

## Slide 38
Decryption
9
Rounds?
No
Yes
128 Bit Input
128 Bit Output
Add Round Key
Inverse Shift Row
Inverse
Substitution
Bytes
Inverse Substitution Bytes
Add Round Key
Inverse Mix Col
Inverse Shift Row
Add Round Key

## Slide 39
Initial
Mid
Final
Circuits
Add Round Key
Inverse
Substitution
Bytes
Inverse Substitution Bytes
Add Round Key
Inverse Mix Col
Inverse Shift Row
Add Round Key
Inverse Shift Row

## Slide 40
Initial
Mid
Final
Mid
Mid
Mid
Mid
First
Between
Last
FSM Circuits

## Slide 41
Decrypter
First
Between
Last
Between
Between
128 Bit Processed Data
Completion Status
Data
Data
Data
Data
Data
Data_in
Data_out

## Slide 42
E
N
C
R
Y
P
T
E
R
R
E
C
E
I
V
E
R
T
R
A
N
S
M
I
T
T
E
R
D
E
C
R
Y
P
T
E
R
R
E
C
E
I
V
E
R
T
R
A
N
S
M
I
T
T
E
R
Computer
Computer
Python Code
Python Code
Complete Implementation

## Slide 43
Encryption: Simulation
Decryption: Simulation

## Slide 44
Challenges
Without Pipeline
2 Device Pipeline
5 Device Pipeline